## Slide 1: pynga: A python package for the Next Generation Attenuation relations
Feng Wang
Oct. 12th, 2012

## Slide 2
utils.py
__init__.py
Validation & Application
pynga/
AS08.py
BA08.py
CB08.py
CY08.py
SC08.py
Python Classes
Python Package
Returning:
Median
Inter-event standard deviation
Intra-event standard deviation
total standard deviation
Features:
Easy to install and less dependence on other packages
Capable to input updated coefficients and keep using the same model functionals
Capable of adding new NGA models
Build-in utilities to compute unknown parameters, such as Rjb, Rrup, and Rx based on fault geometry
Output results can be easily saved as Mat-style for further usages
Python utilities
Download:
The package is version-controlled at GitHub, so you can clone the package using "git clone"
git clone git@github.com:fengw/pynga.git
Package components

## Slide 3
Validation of NGA models
Compare median and total standard deviation with those calculated using OpenSHA
Results are presented in
pynga/Validation/plots/ValiationNGAs
RMS is within 0.02% for PGA, PGV, and SA at various periods

## Slide 4
Distance calculations
UCERF-type fault geometry
Basic inputs:
  1.Surface projection of top rupture edges
  (single and/or multiple fault traces, long/lat)
  2.Average upper seismogenic depth (km)
  3.Average lower seismogenic depth (km)
  4.Average dip angle (degree)
utils.py provides functions to generate fault surface and discretize the surface by specifying down-dip and along-strike grid spaces, and then to compute distance parameters (Rjb, Rrup, Rx) given site location.

## Slide 5
BBP-type fault geometry
For more complicated source descriptions (in *.srf, discretized points are explicitly presented on the fault plane, just like rupture variations used in CyberShake which are similar to *.srf)
utils.py provides functions to generate fault surface (different choices) and discretize the surface by specifying down-dip and along-strike grid spaces, and then to compute distance parameters (Rjb, Rrup, Rx) given site location.
A simple source description shown in *.src file

## Slide 6
Examples
BBP-type fault geometry
A simple source
from Fling
study

## Slide 7
Examples

## Slide 8
Examples

## Slide 9
Examples

## Slide 10
Calcluated by OpenSHA
Examples
SRF-type fault geometry

## Slide 11
SRF-type fault geometry
Calcluated by utils.py in pynga
Examples